## Slide 1
The Learning Channel
The Learning Channel
Notes: Layer 1: Physical cables such as Twisted pairs, Fiber optic, Coax plus Wireless devices define Layer 1.
Layer 2: A place where we move traffic from one device to another (i.e. segments).
Layer 3: IP addressing and Routing allows us move data across longer distances.

## Slide 2
Cilium Kubernetes CNI Provider Deep Dive: Part 1
Agenda
What is Cilium?
Iptables performance issues
eBPF overview
How Cilium leverages eBPF for load balancing
Cilium installation step by step
Notes: Layer 1: Physical cables such as Twisted pairs, Fiber optic, Coax plus Wireless devices define Layer 1.
Layer 2: A place where we move traffic from one device to another (i.e. segments).
Layer 3: IP addressing and Routing allows us move data across longer distances.

## Slide 3
What is Cilium?
Networking
Observability
Security
Service Mesh
(Beta)
CNI provider
“Hubble” provides distributed networking and security observability
L3/4 , L7, and DNS based network polices
L7 traffic management & load-balancing, TLS termination, etc.
Notes: Layer 1: Physical cables such as Twisted pairs, Fiber optic, Coax plus Wireless devices define Layer 1.
Layer 2: A place where we move traffic from one device to another (i.e. segments).
Layer 3: IP addressing and Routing allows us move data across longer distances.

## Slide 4
Control Plane
API Server
Controller Manager
Scheduler
etcd
Kubelet
CNI Plug-in
eth0
192.168.0.2
Worker Node
POD Network Name Space
10.244.0.2
CRI
Container Runtime
POD
Kube-Proxy
Host Network Name Space
eth0
192.168.0.22
kube-node1
Kube-Proxy
eth0
192.168.0.20
eth0
192.168.0.2
POD Network Name Space
Host Network Name Space
eth0
192.168.0.26
kube-node2
Kube-Proxy
iptables
172.16.9.68:8080
172.16.209.144:8080
Hello-world svc
ClusterIP
10.101.86.173:80
iptables Kube-Proxy Mode Performance Issues for Large Kubernetes Installations
iptables
ClusterIP
10.101.86.173:80
172.16.9.68:8080
172.16.209.144:8080
POD
HelloWorld
Kubelet
eth0
172.16.9.68
CRI
CNI
POD Network Name Space
Kubelet
POD
HelloWorld
eth0
172.16.209.144
CRI
CNI
POD Network Name Space
terminal
kube-master
Kube-Proxy iptables mode perf Issues (for large installations)
For each service add, multitude of iptables rules must be added.
Tables are not indexed. Sequential search is done to find which chains and rules applied to a packet.
Incremental changes are not supported (Copy all rules, make changes, save back)
It was never designed to be an efficient load balancer in extremely demanding situations.
target prot opt source destination
KUBE-SVC-NPX46M4PTMTKRN6Y tcp -- 0.0.0.0/0 10.96.0.1 /* default/kubernetes:https cluster IP */ tcp dpt:443
KUBE-SVC-TCOU7JCQXEZGVUNU udp -- 0.0.0.0/0 10.96.0.10 /* kube-system/kube-dns:dns cluster IP */ udp dpt:53
KUBE-SVC-ERIFXISQEP7F7OF4 tcp -- 0.0.0.0/0 10.96.0.10 /* kube-system/kube-dns:dns-tcp cluster IP */ tcp dpt:53
KUBE-SVC-JD5MR3NA4I4DYORP tcp -- 0.0.0.0/0 10.96.0.10 /* kube-system/kube-dns:metrics cluster IP */ tcp dpt:9153
KUBE-SVC-I6CTHWSTJGL5RHWT tcp -- 0.0.0.0/0 10.101.86.173 /* default/hello-world-service cluster IP */ tcp dpt:80
target prot opt source destination
KUBE-MARK-MASQ tcp -- 0.0.0.0/0 0.0.0.0/0 /* default/hello-world-service */ tcp dpt:30001
KUBE-SEP-DBUZDH4A34C65KQT all -- 0.0.0.0/0 0.0.0.0/0 /* default/hello-world-service */ statistic mode random probability 0.50000000000
KUBE-SEP-PTQOICECNOXPELPH all -- 0.0.0.0/0 0.0.0.0/0 /* default/hello-world-service */
sudo iptables -n -t nat -L KUBE-SERVICES
sudo iptables -n -t nat -L KUBE-SVC-I6CTHWSTJGL5RHWT
sudo iptables -n -t nat -L KUBE-SEP-DBUZDH4A34C65KQT
target prot opt source destination
KUBE-MARK-MASQ all -- 172.16.209.144 0.0.0.0/0 /* default/hello-world-service */
DNAT tcp -- 0.0.0.0/0 0.0.0.0/0 /* default/hello-world-service */ tcp to:172.16.209.144:8080
sudo iptables -n -t nat -L KUBE-SEP-PTQOICECNOXPELPH
target prot opt source destination
KUBE-MARK-MASQ all -- 172.16.9.68 0.0.0.0/0 /* default/hello-world-service */
DNAT tcp -- 0.0.0.0/0 0.0.0.0/0 /* default/hello-world-service */ tcp to:172.16.9.68:8080
gary@kube-node1:~$
gary@kube-node1:~$
gary@kube-node1:~$
gary@kube-node1:~$
KUBE-SVC-* chain acts as a load balancer, and distributes the packet to KUBE-SEP-* chain equally.
KUBE-SEP-* chain represents a Service EndPoint. It simply does DNAT, replacing service IP:port with pod's endpoint IP:Port.
KUBE-SERVICES is the entry point for service packets. It match the destination IP:port and dispatch the packet to the corresponding KUBE-SVC-* chain.
Notes: -n — Displays IP addresses and port numbers in numeric format, rather than the default hostname and network service format.
-t — Specifies a table name.
-L — Lists all of the rules in the chain specified after the command.
-v — Displays verbose output, such as the number of packets and bytes each chain has seen, the number of packets and bytes each rule has matched, and which interfaces apply to a particular rule.
- P packets while within a Linux host have an attribute called packet mark. That is just a number.
These rules accept packets which have been given a packet mark value 0x1068 or 0x4000 (in the PREROUTING chain of the mangle, raw or nat chains)

## Slide 5
What is eBPF?
eBPF (Extended Berkeley Packet Filter) is a revolutionary technology with origins in the Linux kernel that can run sandboxed programs in an operating system kernel. It is used to safely and efficiently extend the capabilities of the kernel without requiring to change kernel source code or load kernel modules.
Historically, the operating system has always been an ideal place to implement observability, security, and networking functionality. However, an operating system kernel is hard to evolve due to its central role and high requirement towards stability and security.
By allowing to run sandboxed programs within the operating system, application developers can run eBPF programs to add additional capabilities to the operating system at runtime. The operating system then guarantees safety and execution efficiency as if natively compiled with the aid of a Just-In-Time (JIT) compiler and verification engine.
The Linux kernel supports a set of BPF hooks in the networking stack that can be used to run BPF programs. The Cilium datapath uses these hooks to load BPF programs that when used together create higher level networking constructs:
  XDP: The XDP BPF hook is at the earliest point possible in the networking driver and triggers a run of the BPF program upon packet reception.
  Traffic Control Ingress/Egress: BPF programs attached to the traffic control (tc) ingress hook are attached to a networking interface, same as XDP, but will run after the networking stack has done initial processing of the packet.
  Socket operations: The socket operations hook is attached to a specific cgroup and runs on TCP events.
  Socket send/recv: The socket send/recv hook runs on every send operation performed by a TCP socket.
Notes: Layer 1: Physical cables such as Twisted pairs, Fiber optic, Coax plus Wireless devices define Layer 1.
Layer 2: A place where we move traffic from one device to another (i.e. segments).
Layer 3: IP addressing and Routing allows us move data across longer distances.

## Slide 6
eBPF Maps
A vital aspect of eBPF programs is the ability to share collected information and to store state. For this purpose, eBPF programs can leverage the concept of eBPF maps to store and retrieve data in a wide set of data structures. eBPF maps can be accessed from eBPF programs as well as from applications in user space via a system call.
The following is an incomplete list of supported map types :
  Hash tables, Arrays
  LRU (Least Recently Used)
  Ring Buffer
  Stack Trace
  LPM (Longest Prefix match)
Notes: Layer 1: Physical cables such as Twisted pairs, Fiber optic, Coax plus Wireless devices define Layer 1.
Layer 2: A place where we move traffic from one device to another (i.e. segments).
Layer 3: IP addressing and Routing allows us move data across longer distances.

## Slide 7
eBPF Programing
eth0
192.168.0.45
lxc0
All packets that arrive at VM’s network interface (eth0) and are destined for port 80, forward them through the veth pair to the Hello-World service hosted on the POD
clang –target bpf [….]
SEC(“to_netdev”)
int handle(struct sk_buff *skb) {
…
if (tcp->dport == 80)
redirect(lxc0);
return DROP_PACKET;
}
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
User Mode
Kernel Mode
Foo.o
eBPF loader
bpf(BPF_PROG_LOAD,…)
eBPF verifier
JIT
Native Code
BPBF
Maps
eth0
Hello-world
10.0.0.247
POD
LAN
packet
packet
packet
packet
packet
Notes: Layer 1: Physical cables such as Twisted pairs, Fiber optic, Coax plus Wireless devices define Layer 1.
Layer 2: A place where we move traffic from one device to another (i.e. segments).
Layer 3: IP addressing and Routing allows us move data across longer distances.

## Slide 8
kube-master
Control Plane
API Server
Controller Manager
Scheduler
etcd
Kubelet
CNI Plug-in
eth0
192.168.0.2
Worker Node
POD Network Name Space
eth0
10.244.0.2
CRI
Container Runtime
POD
Kube-Proxy
Host Network Name Space
eth0
10.0.0.135
kube-node1
Kube-Proxy
Worker Node
eth0
10.0.0.134
POD Network Name Space
eth0
192.168.9.87
POD (Hello-world)
POD Network Name Space
eth0
192.168.9.86
POD (Hello-world)
Kubelet
CNI Plug-in
eth0
192.168.0.2
Worker Node
POD Network Name Space
eth0
10.244.0.2
CRI
Container Runtime
POD
Kube-Proxy
Host Network Name Space
eth0
10.0.0.164
kube-node2
Kube-Proxy
POD Network Name Space
eth0
192.168.233.207
POD (hello-world)
iptables
192.168.9.87:8080
192.168.9.86:8080
POD Network Name Space
eth0
192.168.233.206
POD (hello-world)
192.168.233.206:8080
192.168.233.207:8080
Hello-world svc
Hello-world End points:
10.0.1.62:8080 10.0.1.75:8080 10.0.0.183:8080
10.0.0.188:8080
ClusterIP
10.107.72.75:8080
Service Load Balancing and eBPF (Part 1)
iptables
ClusterIP
10.107.72.75:8080
192.168.9.87:8080
192.168.9.86:8080
192.168.233.206:8080
192.168.233.207:8080
(iptables mode)
(iptables mode)
(ipvs mode)
(ipvs mode)
IPVS
IPVS
Cilium Agent
Cilium Agent
eBPF
SVC
MAP
eBPF
SVC
MAP
Service IP | Port | ID | Endpoint ID | Endpoint IP | Port
10.107.72.75
10.107.72.75
10.107.72.75
10.107.72.75
8080
8080
8080
8080
1
1
1
1
4
5
6
7
10.0.1.62
10.0.1.75
10.0.0.183
10.0.0.188
8080
8080
8080
8080
Notes: Kubectl generates a manifest describing a Deployment
The manifest is sent to the API Server
The manifest is validated by the API Server, and persisted to “etcd”

## Slide 9
eBPF Programing
curl http://10.107.72.75:8080
Linux kernel
eth0
192.168.0.40
lxce9626b0b3d0c
eth0
Hello-world SVC
10.0.1.183
eth0
Hello-world SVC
10.0.1.184
lxc142af750fbe9
eth0
Hello-world UI
10.0.0.247
lxcc4b87faa7e82
Service
Connection
Identity
Policy
Endpoint
ClusterIP
10.107.72.75 :8080
eBPF: lxcc4b87faa7e82
#
cilium_vxlan
cilium_vxlan
eBPF Service Has Map
Service IP | Port | ID | Endpoint ID | Endpoint IP | Port
10.107.72.75 | 8080 | 1 | 4 | 10.0.1.183 | 8080
10.107.72.75 | 8080 | 1 | 5 | 10.0.1.184 | 8080
eBPF Conn Track Map
Source IP | Source Port | Dest IP | Dest Port | Type | Endpoint ID | Service ID
10.0.0.247 | 4321 | 10.107.72.75 | 8080 | SVC | 4 | 
10.0.0.247 | 4321 | 10.0.1.183 | 8080 | Egress |  | 1
POD
POD
POD
Source: 10.0.0.247
Destination: 10.107.72.75
Port: 8080
Payload: Request
IP Packet
eth0
192.168.0.45
Source: 10.0.0.247
Destination:
Port: 8080
10.0.1.183
Payload: Request
IP Packet
Source: 10.0.0.247
Destination:
Port: 8080
10.0.1.183
Payload: Request
IP Packet
Source: 10.0.0.247
Destination:
Port: 8080
10.0.1.183
Payload: Request
IP Packet
Source: 10.0.0.247
Destination:
Port: 8080
10.0.1.183
Payload: Request
IP Packet
Source: 10.0.0.247
Destination:
Port: 8080
10.0.1.183
Payload: Request
IP Packet
Source: 10.0.0.247
Destination:
Port: 8080
10.0.1.183
Payload: Response
IP Packet
Source: 10.0.1.184
Destination:
Port: 8080
10.0.0.247
Payload: Response
IP Packet
Source: 10.0.1.184
Destination:
Port: 8080
10.0.0.247
Payload: Response
IP Packet
Source: 10.0.1.184
Destination:
Port: 8080
10.0.0.247
Payload: Response
IP Packet
Source: 10.0.1.184
Destination:
Port: 8080
10.0.0.247
Payload: Response
IP Packet
Source: 10.0.1.184
Destination:
Port: 8080
10.0.0.247
Hello, world!
Version: 1.0.0
Hostname: hello-world-57fbf88c7-xv75x
eBPF Conn Track Map
Source IP | Source Port | Dest IP | Dest Port | Type | Endpoint ID | Service ID
10.0.0.247 | 4321 | 10.107.72.75 | 8080 | SVC | 4 | 
10.0.0.247 | 4321 | 10.0.1.183 | 8080 | Egress |  | 1
Payload: Response
IP Packet
Source:
Destination:
Port: 8080
10.0.0.247
10.107.72.75
Do we already have an established connection?
IP to ID Mapping
IP: 10.0.0.247
ID: 848
Is ID 848 allowed on port 8080?
Service Load Balancing and eBPF (Part 2)
Notes: Layer 1: Physical cables such as Twisted pairs, Fiber optic, Coax plus Wireless devices define Layer 1.
Layer 2: A place where we move traffic from one device to another (i.e. segments).
Layer 3: IP addressing and Routing allows us move data across longer distances.

## Slide 10
Cilium Installation
Agent
Hubble
Cilium CLI
Operator
CNI Plugin
Server
Relay
CLI
UI
Agent: Runs on each node in the cluster and listens for events from orchestration systems such as Kubernetes to learn when containers or workloads are started and stopped. It also manages the eBPF programs which the Linux kernel uses to control all network access in / out of those containers.
The Cilium CLI is a command-line tool that is installed along with the Cilium agent. It interacts with the REST API of the Cilium agent running on the same node. The CLI allows inspecting the state and status of the local agent. It also provides tooling to directly access the eBPF maps to validate their state.
The Cilium Operator is responsible for managing duties in the cluster which should logically be handled once for the entire cluster, rather than once for each node in the cluster.
The Hubble server: runs on each node and retrieves the eBPF-based visibility from Cilium. It is embedded into the Cilium agent in order to achieve high performance and low-overhead. It offers a gRPC service to retrieve flows and Prometheus metrics.
Relay (hubble-relay) is a standalone component which is aware of all running Hubble servers and offers cluster-wide visibility by connecting to their respective gRPC APIs and providing an API that represents all servers in the cluster.
Notes: Layer 1: Physical cables such as Twisted pairs, Fiber optic, Coax plus Wireless devices define Layer 1.
Layer 2: A place where we move traffic from one device to another (i.e. segments).
Layer 3: IP addressing and Routing allows us move data across longer distances.